## Slide 1
Robust Multi-Robot Mapless Navigation in Dynamic Hospital Environments with Accurate Intention Inference, Trajectory Prediction, and Explainable AI
Presented by: Naveen Kumar
Supervisor:
Prof. Dr. Amar Behera
Date: July 2026

## Slide 2
Hospital Social Navigation
Slide 2
Synthesizing state-of-the-art sensory architectures and learning pipelines to safely pilot robots in dynamic hospital environments.
Autonomous Framework: Build a complete model for navigation inside unpredictable human environments.
State Construction: Aggregate spatial, human tracking, and odometry metrics comprehensively.
Social Safety: Learn dynamic policies obeying human social boundaries.
4
SENSOR INPUTS
160D
STATE SPACE
PPO
OPTIMIZED CONTROL POLICY
Core Research Objectives

## Slide 3
Hospital Social Navigation
Slide 3
Simulation Platform
ROS2 Jazzy & Gazebo Harmonic: Real-time hardware emulation in a dynamic hospital world with moving pedestrians and nurse stations.
Robot Base: Custom TurtleBot3-inspired differential chassis mapped to real-time odometry metrics.
Active Sensor Topics
3D LiDAR — /velodyne_points
Depth Camera — /depth/image_raw
IMU Sensor — /imu
Wheel Encoder — /joint_states
Gazebo Environment & Sensor Suite

## Slide 4
LiDAR Encoder: PointNet++
We utilize hierarchical feature extraction to process raw 3D point clouds into a compact 64D embedding.
PointNet++ Stages
1. Input (1024 points)
2. Set Abstraction (SA) Layers
3. Global Feature Aggregation
4. Output Embedding (64D)
Sampling: Downsamples Raw points to 1024 points
Grouping: Captures local neighborhoods
Projection: MLP reduces 1024D to 64D

## Slide 5
Hospital Social Navigation
Slide 5
Feature Generation Map
Spatial Geometry Mapping
The CNN encoder directly processes camera frames to understand scene layout. This acts as a secondary layer of protection against highly reflective or transparent objects that confuse traditional LiDAR scanners.
Key Spatial Signals
Input Frame Acquisition
Reads raw image matrices via /depth/image_raw
CNN Feature Backbone
Processes structural patterns, edges, and objects
Feature Map Projection
Outputs compressed 64-Dimensional Depth Features
Captures near-obstacle 3D geometries.
Formulates pixel-to-obstacle distance metrics.
Provides structural context for narrow hallways.
PROCESSING PIPELINES DEPTH IMAGE PROCESSING
Depth Camera Processing Pipeline

## Slide 6
Hospital Social Navigation
Slide 6
Tracks continuous, high-frequency orientation trends.
Prevents cumulative odometry drift errors over run-times.
IMU Encoder
Handles linear acceleration, angular velocity, and inertial heading variations to prevent slide slip.
Wheel Encoder
Collects continuous speed steps via joint state subscriptions to record real robot speed commands.
PROCESSING PIPELINES KINEMATICS & INERTIAL NAVIGATION
Kinematic Pipelines: IMU & Wheel Encoder

## Slide 7
Hospital Social Navigation
Slide 7
PointNet++ Output
CNN Output
MLP + Upscale
MLP + Upscale
Dimension Expansion & Linear Steps
Kinematic vectors (IMU & Wheel) are upscaled using dense linear layers from 32D to 64D before concatenation to align temporal influence across sensory modes.
Unified Output Projection
Outputs a clean, rich 128-Dimensional Fused Feature vector.
This compressed space encapsulates raw spatial maps, structural features, and kinematic states into a unified, high-density observation vector.
ARCHITECTURE LAYOUT MULTI-MODAL ATTENTION FUSION
Multi-Modal Sensor Fusion

## Slide 8
Hospital Social Navigation
Slide 8
Pipeline Output: Compressed 30-Dimensional Human Feature Matrix
Human Detection Layer
Segment camera frames & scans to isolate pedestrians.
Dynamic Localization
Transforms coordinates into the base robot frame. Calculates Euclidean distance and bearing angle.
Kalman Identification
Associates targets across sequential frames to maintain track continuity.
PERCEPTION STACK PEDESTRIAN MONITORING
Human Detection, Localization & Tracking

## Slide 9
Kalman Filter State Prediction
State Vector:
Transition Matrix:
Future Prediction
Predicting position at time :
Used to generate safe navigation buffers around humans.
The system maintains active tracking estimates during occlusions, preventing the robot from 'forgetting' pedestrians when they step briefly behind nurse desks or visual blockages.
Robust Tracking Benefits
Smoothes raw sensor noise and coordinate jitter.
Prevents navigation policy breakdown.
Sustains pedestrian IDs across frames.

## Slide 10
Hospital Social Navigation
Slide 10
Evaluation Inputs
The intention module continuously evaluates key motion properties of pedestrians:
Prediction Targets
Forecasts behaviors over a short-term future window:
Navigation Safety
Predicting paths reduces proactive collision risks and prevents freezing-robot issues in crowded corridors.
Enables active deceleration or path corrections early.
Speed & Heading Angle
Trajectory History Logs
Orientation changes
Projected path direction
Dynamic velocity trends
Human-Robot space intersection
Human Intention Prediction
LEFT
Predicted path crossing.
RIGHT
Trajectory adjustment.
STOP
Speed < 0.05 m/s
Stationary obstacle.

## Slide 11
Hospital Social Navigation
Slide 11
A unified aggregator subscribes to all independent processing modules and concatenates features into a comprehensive state representation vector.
Vector Concatenation
128D + 30D + 2D = 160D Vector
This combined array constructs a complete environmental, personal, and target space footprint.
ROS2 Output Stream
Topic Name: /ppo_state
Array Dimension: [160, 1]
Update rate: 20 Hz Sync Cycle
DATA ASSEMBLER STATE AGGREGATOR & SPACE
State Aggregator (Total Feature Space)

## Slide 12
Hospital Social Navigation
Slide 12
Actor-Critic Architecture
Splits the unified state vector into actor policy distributions and state value assessments.
Reward Function Formulation
The reinforcement policy optimization relies on a balanced multi-objective reward structure:
Goal Progress: Positive reward on distance reduction.
Collision Penalty: Severe penalty on obstacle contact.
Smooth Motion: Penalizes jittery or erratic velocity changes.
Social Space Penalty: Discourages personal space encroachment.
DECISION MAKING PPO ARCHITECTURE & OPTIMIZATION
Proximal Policy Optimization (PPO) Network

## Slide 13
Hospital Social Navigation
Slide 13
CUDA & PointNet++
CUDA-dependent custom operators caused build failures and compatibility issues with the ROS 2 setup.
Resolution: Implemented a lightweight CPU-compatible encoder as a stable fallback.
Gazebo Simulation Freezing
Multi-sensor processing and PPO training caused simulation slowdown.
Resolution: Optimized update frequencies and reduced computational overhead.
Dynamic Synchronization
Each sensor pipeline (LiDAR, Depth, IMU, Odometry) updated asynchronously, causing fusion lag.
Resolution: Used MessageFilters approximate-time policies to align topics.
EXECUTION DIAGNOSTICS CHALLENGES & RESOLUTIONS
Challenges Faced & Resolutions

## Slide 14
Hospital Social Navigation
Slide 14
All core layers of the perception, localization, fusion, state-aggregator, and training pipelines are fully implemented.
Sensory Encoders: Verified independent pipelines for 3D LiDAR, depth, and dynamics.
Tracking Layer: Completed Kalman trajectory smoothing.
Fusion Module: Active attention model mapped to 128D space.
Training Baseline: Concurrent PPO training and sensor processing increased computational overhead, leading to Gazebo freezes and low real-time factor.
ROS 2 Jazzy Integration
Full communication loops between nodes and Gazebo Harmonic simulation are established and verified.
PROJECT BENCHMARKING COMPLETED PIPELINE CHECKLIST
Project Status & Accomplishments

## Slide 15
Thank You!
Questions & Discussion